## Slide 1
Rota-Flex™
Pin Box
Leaf Spring Systems
CRE3000 TANDEM INSTALLATION INSTRUCTIONS
Rota-Flex™ Pin Box Installation and Owner’s Manual
A: 135 ft-lb (15/16” socket, 15/16” wrench)
B: 80 ft-lb (3/4” socket)
Wheel Lug Nuts
120 ft-lb (3/4” socket) - See torque pattern
Lippert Hydraulic Jack Mounting Bolt Specification
Fifth Wheel: 90 ft-lb (3/4” socket, 3/4” wrench) (1/2-20 Grade 8 Bolts )
Travel Trailers:
  Tongue Jack: 30 ft-lb (BAL 5.3LS)
  Rear Leveling Jacks: 90 ft-lb (BAL 5.3LS)
  Stabilizer Jacks: 30 ft-lb
Jacks & Stabilizers:
Dexter Operation & Service manual
Quick Reference Torque Guide
A: 70 ft-lb (3/4” socket on bolt, 7/8” wrench)
B: 75 ft-lb (3/4” socket)
C: 120 ft-lb (3/4” socket)
D: 120 ft-lb (15/16” socket on bolt, 15/16” wrench)
Lippert requirement: Torque wrench on bolt head only.
Rev: 3/10/2025
A: Shock mtg bolts: 30 ft-lb (9/16” socket)
B: Trailing Arm Bolt: 200 ft-lb (15/16” socket on bolt, 15/16” wrench)
C: Track Bar Bolt: 80 ft-lb (3/4” socket on bolt, 3/4” wrench)
D: Bump Stop Nut: Tight against metal (5/8” socket)
A
B
C
D
CURT Touring Coil Suspension HD
Service Manual: Touring Coil Suspension HD
Notes:
Lippert requirement: Torque wrench on bolt head only.
U-Bolts torqued to 100 ft-lb w Loctite at factory. No adjustment needed.
Helux Pin Box Maintenance Manual
Helux
Pin Box
This guide is for reference only and includes some components that are not used on every Alliance RV product line. Please verify you are referencing the proper components used on your specific coach.
BAL 5.3LS User Manual
All leaf spring systems constructed similarly, regardless of equalizer. All torque values identical per location.
NOTE: Dexter U-BOLT systems using Flanged nuts require 100 ft‑lb